## Slide 1: Module-2 CSEN 3104 Lecture 11
Dr. Debranjan Sarkar

## Slide 2: Vector Processing

## Slide 3: What is Vector Processing?
In matrix algebra, a vector a = [a1,a2,a3,….,an]T is a column of numbers
The scalars ai are the elements of vector a
In computer technology, a vector is an ordered set of scalar data items, all of the same type, stored in memory
Usually, the vector elements are ordered to have a fixed addressing increment between successive elements, called the stride
A vector processor is a central processing unit that can work on an entire vector in one instruction, whereas the instructions of a scalar processor operate on single data items
In vector processing, arithmetic and logical operations are applied to vectors
The conversion from scalar code to vector code is called vectorization

## Slide 4: What is Vector Processing?
The instruction to the processor is in the form of one complete vector instead of its element
The operand to the instructions are complete vectors instead of one element
Vector processors reduce the fetch and decode bandwidth as the number of instructions fetched are less
Reduces software overhead for maintenance of looping control
Enhanced performance but increased hardware and compiler cost
A compiler capable of vectorization is called vectorizing compiler
Vector processors can greatly improve performance on certain applications e.g. numerical simulation and similar tasks e.g. long-range weather forecasting, aerodynamics and space flight simulation etc.

## Slide 5: Scalar vs. Vector CPU
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
v1
v2
v3
+
vector
length
addv v3, v1, v2
VECTOR
(N operations)
Notes: 25

## Slide 6: Types of Vector Architectures
Memory-memory vector processors
  all vector operations are memory to memory
  There is no limitation of size
  Speed is comparatively slow
  The hardware cost is low
  Example: TI-ASC, CDC STAR-100, and Cyber-205
Vector-register processors
  all vector operations are between vector registers (except load and store)
  Vector equivalent of load-store architectures
  Register to register architecture has limited size
  Speed is very high as compared to the memory to memory architecture.
  The hardware cost is high
  Example: Cray-1, Fujitsu VP-200, Hitachi HITAC S-810, NEC SX-9

## Slide 7: Components of a Vector Processor
Vector Register: A set of registers for all vector operations (except load and store)
  typically 8-32 vector registers, each holding 64-128 64-bit elements
  In vector-register architecture, operands are read into vector registers from which they are fed to the functional units and results of operations are written to vector registers
Vector Functional Units (FUs)
  fully pipelined
  start new operation every clock
  FP add, FP multiply, FP reciprocal, integer add, logical, shift
  may have multiple of same unit
Vector Load-Store Units (LSUs)
  fully pipelined unit to load or store a vector
  there may be multiple LSUs
Scalar registers
  single element for FP scalar or address
Cross-bar
  to connect FUs , LSUs, registers
Show the Vector Register Architecture

## Slide 8: Vector Instruction Types
Six types:
  Vector-vector instructions
    f1: Vj → Vi Example: V1 = sin(V2)
    f2: Vj X Vk → Vi Example: V3 = V1 + V2
  Vector-scalar instructions
    f3: s X Vk → Vi Example: s X V1 = V2
  Vector-memory instructions
    f4: M → V Vector Load
    f1: V → M Vector Store
  Vector reduction instructions
    f6: V → s Find maximum, minimum, sum, mean of all elements of a vector
    f7: Vi X Vj → s Dopt product of two vectors
  Gather and scatter instructions
  Masking instructions

## Slide 9: What is a sparse vector?
A sparse vector is a vector, most of the elements of which are zero
It is inefficient to use a one-dimensional array to store a sparse vector
It is also inefficient to add elements whose values are zero in forming sums of sparse vectors
Gather, Scatter and masking instructions are very useful in handling sparse vectors or matrices
Advanced vector processors implement these instructions directly in hardware

## Slide 10: Gather, Scatter, Masking Instructions
Gather and scatter instructions
  f8: M → V1 X V0 Gather
  f9: V1 X V0 → M Scatter
Gather fetches from memory the non-zero elements of a sparse vector using indices that themselves are indexed
Scatter stores into memory a vector in a sparse vector whose non-zero entries are indexed
The vector register V1 contains the data and the vector register V0 is used as an index to gather or scatter data from or to random memory locations
Masking Instructions
  f10: V0 X Vm → V1
This instruction uses a mask vector to compress or to expand a vector to a shorter or longer index vector

## Slide 11: Thank you