## Slide 1: Module-2 CSEN 3104 Lecture 13
Dr. Debranjan Sarkar

## Slide 2: SIMD Architecture

## Slide 3: Flynn’s classification
Single Instruction Stream Single Data Stream (SISD)
  Conventional machines with single CPU
  Capable of only scalar arithmetic
  mI = mD = 1
Single Instruction Stream Multiple Data Stream (SIMD)
  Single program control unit and many independent execution units
  Example: Illiac IV
  mI = 1, mD > 1
Multiple Instruction Stream Single Data Stream (MISD)
  Several CPUs process the same data using different programs
  Fault tolerant computers
  mI > 1, mD = 1
Multiple Instruction Stream Multiple Data Stream (MIMD)
  Computers with more than one CPU with the ability to execute several programs simultaneously
  Multi Processors containing two or more CPUs that cooperate on common computational tasks
  mI > 1, mD > 1
M
Instruction stream
Data stream
P
mI : minimum number of active instruction streams
mD : minimum number of active data streams

## Slide 4: SIMD Array Processor
A synchronous array of parallel processors
Consists of multiple processing elements (PEs) under the supervision of one control unit (CU)
Can handle single instruction and multiple data (SIMD) streams
Specially designed to perform vector computations over matrices or arrays of data
Two basic architectural organizations of SIMD computers
  Array processors using distributed memories
  Associative processors using content-addressable (or associative) memory
Two configurations of Array Processors
  Illiac IV (developed by the Illinois Automatic Computer team of University of Illinois)
  Burroughs Scientific Processor (BSP)

## Slide 5: Configuration of Illiac IV
Show the block diagram
N numbers of identical synchronized processing elements (PEs) which can concurrently do the same operation on different data
All these PEs are under the control of one CU
Each PE is basically an ALU with working registers and local memory (PEM) for the storage of distributed data
The CU has its own main memory for the storage of programs
The system and user programs are executed under the control of CU
Scalar and control type instructions are executed in the CU
Vector instructions are broadcast to the PEs for distributed execution
Thus spatial parallelism is achieved through multiple arithmetic units (PEs)

## Slide 6: Configuration of Illiac IV
All the PEs perform the same function synchronously in a lock-step fashion under the command of the CU
Vector operands are distributed to the PEMs before parallel execution in the array of PEs
The distributed data can be into the PEMs from an external source via the system data bus or via the CU in a broadcast mode using the control bus
Masking schemes are used to enable or disable each PE to participate in the execution of a vector instruction
Data exchanges among the PEs are done via an interconnection network which performs all necessary data routing and manipulation functions
This interconnection network is under the control of CU

## Slide 7: Configuration of Illiac IV
The Array Processor is normally interfaced to a host computer through the CU
The host computer is a general purpose machine which serves as the operating manager of the entire system, consisting of the host and the processor array
The functions of the host computer include resource management, peripheral and IO supervision
The control unit of the processor array directly supervises the execution of programs, whereas
The host machine performs the executive and IO functions with the outside world
So, an array processor can be considered a back-end attached computer

## Slide 8: SIMD Computer
AN SIMD computer is characterized by a set of parameters:
C = <N, F, I, M>
N = Number of processing elements (PEs) in the system. For Illiac IV, N = 64
F = a set of data routing functions provided by the interconnection network
I = the set of machine instructions for scalar-vector, data routing, and network manipulation operation
M = the set of masking schemes, where each mask partitions the set of PEs into two disjoint subsets of enabled PEs and disabled PEs
This model provides a common basis for evaluating different SIMD machines

## Slide 9: Components in a Processing Element (PEi)
Show figure
Each PEi has
  its own memory PEMi
  A set of working registers and flags (Ai,Bi, Ci and Si)
  An Arithmetic and Logic Unit (ALU)
  A local Index Register (Ii), an address register (Di) and a data routing register (Ri)
  The Ri of each PEi is connected to the Rj of other PEs via the interconnection network
  During data transfer among PEs, the contents of the Ri registers are transferred
  The inputs and outputs of the Ri are totally isolated
  The ith PE is denoted by PEi where the index i is the address of PEi
  Let the total number of PEs be N = 2m, then m = log2N binary digits are needed to encode the address of a PE
  The address register Di is used to hold the m-bit address of the PEi
  Some array processors may use two routing registers – one for input and the other for output

## Slide 10: Masking
During each instruction cycle, each PEi is either
  in the active mode, or
  in the inactive mode
In case a PEi is active, it executes the instruction, broadcast to it by the CU, otherwise it won’t
The masking schemes are used to specify the status flag Si of PEi
Si = 1 indicates an active PEi and Si = 0 indicates an inactive PEi
In the CU, there is a global
  index register (I) and
  N-bit masking register (M)
The collection of Si flags for i = 0, 1, 2, …., N-1 forms a status register S for all the PEs
The bit patterns in registers M and S are exchangeable under the control of CU when masking is to be set

## Slide 11: Thank you