## Slide 1: Module-2 CSEN 3104 Lecture 14
Dr. Debranjan Sarkar

## Slide 2: SIMD Architecture

## Slide 3: Use of indexing to address the local memories in parallel at different local addresses
Consider an array of n X n data elements:
A = {A(i,j), 0 ≤ i, j ≤ (n-1)}
Elements of jth column of A are stored in n consecutive locations of PEMj [say from location 200 to location (200+n-1)] (assume n ≤ N)
We want to access the principal diagonal elements A(j,j) for j=0, 1 , …, (n-1) of the array A
The CU must generate and broadcast an effective memory address 200
The local index registers must be set to be Ij = j for j = 0, 1, …, (n-1) in order to convert the global address 200 to local address 200 + Ij = 200 + j for each PEMj
Within each PE, there is a separate memory address register for holding these local addresses

## Slide 4: Data Routing Mechanisms
Execution of the following vector instruction in an array of N processing elements (PEs)
The sum S(k) of the first k components in a vector A = (A0, A1, …….., An-1) is desired for each k from 0 to (n-1)
We need to compute the following n summations:
k
S(k) = ∑ Ai for k = 0, 1, ……, (n-1)
i=0

## Slide 5: Data Routing Mechanisms
These n vector summations can be computed recursively by going through the following (n-1) iterations:
S(0) = A0
S(k) = S(k-1) + Ak for k = 1, 2,……, (n-1)
For n = 8, the above recursive summation is implemented in an array processor with N = 8 processing elements (PEs)
Log2n = 3 steps are required
Both data routing and PE masking are used
Show diagram
Initially each Ai, residing in PEMi is moved to the Ri register in PEi for i = 0,1,2,…,7

## Slide 6: Data Routing Mechanisms
In the first step, Ai is routed from Ri to Ri+1 and added to Ai+1 with the resulting sum Ai + Ai+1 in Ri+1 for i = 0,1,2,…,6
In step 2, the intermediate sums in Ri are routed to Ri+2 for i = 0 to 5
In step 3, the intermediate sums in Ri are routed to Ri+4 for i = 0 to 3
Thus, the final value of PEk will be S(k) for k = 0,1,2,…,7

## Slide 7: Data Routing Mechanisms
In step 1, PE7 is not involved in data routing (receiving but not transmitting)
In step 2, PE7 and PE6 are not involved in data routing
In step 3, PE7, PE6, PE5 and PE4 are not involved in data routing
These unwanted PEs are masked off during the corresponding steps
During the addition operations
  PE0 is disabled in step 1
  PE0 and PE1 are made inactive in step 2
  PE0, PE1, PE2 and PE3 are masked off in step 3
The PEs that are masked off in each step depend on the operation (data-routing or addition)
Thus the masking pattern keep changing in different operation cycles
Masking and routing operation are much more complicated when the vector length n > N

## Slide 8: Thank you