## Slide 1: Module-2 CSEN 3104 Lecture 15
Dr. Debranjan Sarkar

## Slide 2: Interconnection Networks

## Slide 3: Inter-PE Communication
The design of the architecture of an interconnection network for an SIMD machine is based on
  Operation modes
  Control strategies
  Switching methodologies
  Network topologies

## Slide 4: Operation Modes of Interconnection Network
Synchronous mode
  To establish synchronous communication path for
    Data manipulating function
    Data instruction broadcast
Asynchronous mode
  To have asynchronous communication when
    Connection requests are issued dynamically
Combined mode
  To facilitate both synchronous and asynchronous processing
SIMD machines work in synchronous operation mode, where lock-step operations among all PEs are enforced

## Slide 5: Control Strategy
Interconnection network consists of
  A number of switching elements, and
  Interconnecting links
Interconnection functions are realized by properly setting control of the switching elements
Two types of control
  Centralized control -> the control setting function is managed by a centralized controller
  Distributed control -> the control setting function is managed by the individual switching element
SIMD machines have interconnection networks with centralized control on all switching elements by the control unit

## Slide 6: Switching methodology
Circuit switching
  Physical path is actually established between a source and a destination
  Much more suitable for bulk data transmission
Packet switching
  Data is put in a packet and routed through the interconnection network
  No physical connection is established
  More efficient for many short data messages
Integrated switching
  Includes the capabilities of both circuit switching and packet switching
SIMD interconnection networks assume circuit switching

## Slide 7: Network topology
A network is depicted by a graph in which nodes represent switching points and edges represent communication links
Static topology
  Links between two processors are passive
  Dedicated buses cannot be reconfigured for direct connections to other processors
Dynamic topology
  Can be reconfigured by setting the network’s active switching elements
SIMD interconnection networks are classified into two categories, based on network topologies:
  Static networks
  Dynamic networks

## Slide 8: Static Networks
Topologies in the static networks are classified according to the dimensions required for the layout
    One-dimensional (Linear array)
    Two dimensional (Ring, star, tree, mesh and systolic array)
    Three dimensional (Completely connected, Chordal ring,
    3-cube, 3-cube-connected cycle)
    Hypercube
Show the diagrams

## Slide 9: Dynamic Networks
Single stage dynamic network (show figure)
    N number of input selectors (IS) and N output selectors (OS)
    Each IS is essentially a 1-to-D demultiplexer (1 ≤ D ≤ N)
    Each OS is essentially an M-to-1 multiplexer (1 ≤ M ≤ N)
    To establish a desired path, different control signals are applied to all IS and OS selectors
    Data items may have to recirculate through the single stage several times to reach the final destination
    The higher is the hardware connectivity, the less is the number of recirculations required
    Crossbar-switching network is a single-stage n/w with D=M=N
    Crossbar is an extreme case in which only one circulation is required for any path

## Slide 10: Mesh-connected Illiac Network
Show figure
Single stage recirculating network with N = 64 PEs
In one circulation step, each PEi is allowed to send data to any one of PEi+1, PEi-1 , PEi+r and PEi-r
In practice, N is a perfect square and r = sqrt(N). For Illiac IV, r = 8
The interconnection network of Illiac IV is characterized by the following four routing functions:
  R+1(i) = (i+1) mod N
  R-1(i) = (i-1) mod N
  R+r(i) = (i+r) mod N
  R-r(i) = (i-r) mod N
  Where 0 ≤ i ≤ (N-1)

## Slide 11: Mesh-connected Illiac Network
In the reduced Illiac network, the outputs of ISi are connected to the inputs of OSj for j = i+1, i-1, i+r, and i-r
In other words, OSj gets its inputs from ISi for i = j-1, j+1, j-r, and j+r respectively
Each PEi is directly connected to its four nearest neighbours in the mesh network
Permutation Cycle (a b c) (d e) represents the permutation a→b, b→c, c→a and d→e, e→d in a circular fashion within each pair of parentheses
We may write for Horizontal PEs
R+1 = (0 1 2 … N-2 N-1)
R-1 = (N-1 N-2 … 2 1 0)
When the routing function is executed, data is routed as per above only if all PEs in the cycle are active

## Slide 12: Thank you