## Slide 1: Module-2 CSEN 3104 Lecture 16
Dr. Debranjan Sarkar

## Slide 2: Interconnection Networks

## Slide 3: Mesh-connected Illiac Network
Show figure
Single stage recirculating network with N = 64 PEs
In one circulation step, each PEi is allowed to send data to any one of PEi+1, PEi-1 , PEi+r and PEi-r
In practice, N is a perfect square and r = sqrt(N). For Illiac IV, r = 8
The interconnection network of Illiac IV is characterized by the following four routing functions:
  R+1(i) = (i+1) mod N
  R-1(i) = (i-1) mod N
  R+r(i) = (i+r) mod N
  R-r(i) = (i-r) mod N
  Where 0 ≤ i ≤ (N-1)

## Slide 4: Mesh-connected Illiac Network
In the reduced Illiac network, the outputs of ISi are connected to the inputs of OSj for j = i+1, i-1, i+r, and i-r
In other words, OSj gets its inputs from ISi for i = j-1, j+1, j-r, and j+r respectively
Each PEi is directly connected to its four nearest neighbours in the mesh network
Permutation Cycle (a b c) (d e) represents the permutation a→b, b→c, c→a and d→e, e→d in a circular fashion within each pair of parentheses
We may write for Horizontal PEs
R+1 = (0 1 2 … N-2 N-1)
R-1 = (N-1 N-2 … 2 1 0)
When the routing function is executed, data is routed as per above only if all PEs in the cycle are active

## Slide 5: Mesh-connected Illiac Network
For Vertical PEs, we may write
R+r = ∏(i i+r i+2r …. i+N-2r i+N-r), for r =0, 1, 2, …, r-1
R-r = ∏(i+N-r i+N-2r …. i+2r i+r i) , for r =0, 1, 2, …, r-1
In the reduced Illiac network,
R+4 = (0 4 8 12) (1 5 9 13) (2 6 10 14) (3 7 11 15)
R-4 = (12 8 4 0) (13 9 5 1) (14 10 6 2) (15 11 7 3)
The cycle (2 6 10 14) in the above permutation R+4 will not be executed if one or more among PE2, PE6, PE10, and PE14 is disabled by masking
Generally speaking, when R+r or R-r is executed, data are permuted only if PEi+kr, where 0 ≤ k ≤ r-1 are active for each i

## Slide 6: Mesh-connected Illiac Network
The Illiac network is a partially connected network (Show figure)
It is noted that
  In one step, only 4 PEs can be reached from any PE
  PE0 to PE1, PE4, PE12 or PE15
  In two steps, 7 PEs can be reached from any PE
  PE0 to PE2, PE3, PE5, PE8, PE11, PE13 or PE14
  In three steps, 11 PEs can be reached from any PE
  Processing elements PE6, PE7, PE9 or PE10 can be reached from PE0 in the worst case of three steps
It takes I steps (recirculations) to route data from PEi to any other PEj, in an Illiac network of size N, where I is upper-bounded by
I ≤ sqrt(N) – 1
  At most sqrt(64) – 1 = 7 steps are needed in Illiac IV to route data from any one PE to another PE
If connectivity is increased, the upper bound can be lowered

## Slide 7: Single Stage Dynamic Network
Also called recirculating network
Data items may have to recirculate through the single stage several times before reaching their final destination
The number of recirculations needed depends on the connectivity of the network
Generally, the higher the connectivity, the less is the number of recirculations
The crossbar network is an extreme case where only one circulation is needed to establish any connection path
However it is very costly. A fully connected crossbar network has a cost of O(N2) which may be prohibitive for large N
Most recirculating networks have cost O(NlogN) or lower, which is much more cost-effective for large N

## Slide 8: Multistage Dynamic Networks
Many stages of interconnected switches form a multistage network
  Described by 3 characterizing features
    Switch box
    Network topology
    Control structure
  Many switch boxes are used
  Each switch box is basically an interchange device with 2 inputs and 2 outputs (show figure)
  A two function switch box can be in any of the following states
    Straight
    Exchange
  A four function switch box can be in any of the following states
    Straight
    Exchange
    Upper broadcast
    Lower broadcast

## Slide 9: Multistage Networks
Capable of connecting an arbitrary input terminal to an arbitrary output terminal
Consists of n stages where N = 2n is the number of input and output lines
Each stage may use N/2 switch boxes
Each stage is connected to the next stage by at least N paths
The interconnection patterns from stage to stage determine the network topology
The network delay is proportional to the number of stages
The control structure can be
  Individual stage control
    uses the same control signal to set all switch boxes in the same stage.
    Requires n sets of control signals
  Individual box control
    Separate control signal is used to set the state of each switch box
    High flexibility but more cost
  Partial stage control
    Compromise design

## Slide 10: Cube Interconnection Networks
Can be implemented as a
  single-stage (or recirculating) network
  Multistage network
Show figure of a 3-dimensional cube
Horizontal lines (parallel to x-axis) connect vertices (PEs) whose addresses differ in the LSB position
Vertical lines (parallel to y-axis) connect vertices (PEs) whose addresses differ in the MSB position
Lines parallel to z-axis connect vertices (PEs) whose addresses differ in the middle bit position

## Slide 11: Cube Interconnection Networks
The unit cube concept may be extended to an n-dimensional unit space, called n-cube with n-bit address for each vertex
In the n-cube, each PE located at a corner is directly connected to its n neighbours
The addresses of the neighbouring PEs differ in one bit position only
The routing functions of an n-dimensional cube network are given by:
Ci(an-1 ….. a1a0) = an-1 ….. ai+1ai’ai-1 ….. a1a0 for i = 0,1,2, ……, n-1
Examples of cube network
  Pease’s binary n-cube
  The flip network
  Programmable switching network proposed for the Phoenix project

## Slide 12: Cube Interconnection Networks
In the recirculating (single stage) cube network, each ISA (for 0 ≤ A ≤ N-1) is connected to n OSs whose addresses are an-1an-2 ......ai+1ai‘ai-1 ...... a1a0 (for 0 ≤ i ≤ n-1)
Similarly, each OST with T = tn-1tn-2 ...... t1t0 gets its inputs from ISs whose addresses are tn-1tn-2 ......ti+1ti‘ti-1 ...... t1t0 (for 0 ≤ i ≤ n-1)
The n routing functions are given by:
Ci(an-1an-2 ...... a1a0) = an-1an-2 ......ai+1ai‘ai-1 ...... a1a0 (for 0 ≤ i ≤ n-1)
Show the diagram of recirculating cube network
C0 = (0,1) (2,3) (4,5) (6,7)
C1 = (0,2) (1,3) (4,6) (5,7)
C2 = (0,4) (1,5) (2,6) (3,7)
If all the 3 connecting patterns are assembled together, the 3-cube is obtained

## Slide 13: Cube Interconnection Networks
The same set of cube-routing functions may be implemented by a
three-stage cube network (Show figure)
Two-function (Straight and Exchange) switch boxes are used
Stage i implements the Ci routing function
This means the switch boxes at stage i connect an input line to the output line that differs from it only at the ith bit position
Individual box control is assumed in a multistage cube network
Show the path between a source and a destination
Supports up to N one-to-one simultaneous connections
There may be some permutations which cannot be established
Also supports one-to-many connections; that is, an input device can broadcast to all or a subset of the output devices (Show figure)

## Slide 14: Cube Interconnection Networks
We may note that the permutation (0,1) (0,2) (0,4) is performed only if the top row boxes (a, e, i) are set to exchange and the rest are set to straight
Masking may change the data-routing patterns
General practice is to disable all the PEs belonging to the same cycle of a permutation
In case of P2 = (0,4) (1,5) (2,6) (3,7), if both PE2 and PE6 become inactive by masking, the cycles (2,6) are removed and the cube-routing function C2 performs only the partial permutation (0,4) (1,5) (3,7)
If only PE2 is disabled,
  the above partial permutation will still be performed
  Data in both PE2 and PE6 will be transferred to PE2
  PE6 will not receive any data
Masking should be carefully applied to cube networks

## Slide 15: Thank you