## Slide 1: Module-2 CSEN 3104 Lecture 18 20/08/2019
Dr. Debranjan Sarkar

## Slide 2: Interconnection Networks

## Slide 3: Shuffle-Exchange and Omega Networks
Based on two routing functions --- Shuffle (S) and Exchange (E)
Let A = an-1 …. a1a0 be the address of a Processing Element (PE)
The Shuffle function is given by
S(an-1 …. a1a0) = an-2 …. a1a0 an-1 where 0 ≤ A ≤ (N-1) and n = log2N
Corresponds to cyclic shifting of the bits in A to the left for 1 bit position
Show figure for perfect shuffle
This action corresponds to perfect shuffling a deck of N cards
The inverse perfect shuffle does the opposite to restore ordering (Show figure)
Corresponds to cyclic shifting of the bits in A to the right for 1 bit position
The Exchange function is given by
E(an-1 …. a1a0) = an-1 …. a1a0’
The Exchange function exchanges the data between two PEs with adjacent addresses
It is to be noted that E(A) = C0 (A), where C0 was the cube routing function

## Slide 4: Shuffle-Exchange and Omega Networks
The Shuffle-Exchange function can be implemented as
  Single stage network
  Multistage network
Single Stage recirculating shuffle-exchange network (Show figure)
Dashed lines -> Shuffle Solid lines -> Exchange
A number of parallel algorithms can be effectively implemented by using Shuffle-Exchange function. Examples:
  Fast Fourier Transform (FFT)
  Polynomial Evaluation
  Sorting
  Matrix Transposition etc…

## Slide 5: Multistage Omega Networks
To implement Shuffle-Exchange functions (Show figure)
An N X N Omega network consists of n (= log2N) identical stages
Perfect shuffle interconnection between two adjacent stages
Each stage has N/2 numbers of 4-function (straight, exchange, upper broadcast and lower broadcast) switch boxes under independent box control
The switch boxes can be repositioned without violating the perfect shuffle interconnection between stages (Show figure)
The n-cube network has the same interconnection topology as the repositioned Omega
However, they are different in the following two points:
  Cube NW uses 2-function switch boxes, whereas Omega NW uses 4-function ones
  The dataflow directions in the two NWs are opposite to each other i.e. the roles of the input-output lines are exchanged in the two networks

## Slide 6: Routing Algorithm for Omega Network
A source S (with address sn-1 sn-2 . . . s0 ) has to be connected to a certain destination D (with address dn-1 dn-2 . . . d0 )
Starting at input S, connect the input of the first switch [in the (n-1)th stage] that is connected to S to
  the upper output of the switch when dn-1= 0
  otherwise, to the lower output
In the same way, bit dn-2 determines the output of the switch located on the next stage
This process continues until a path is established between S and D
In general, the input of the switch on the ith stage is connected to the upper output when di = 0; Otherwise, the switch is connected to the lower output
Example: Source 2 (i.e., S = 010) and destination 6 (i.e., D =110) (Show Figure)
In addition to one-to-one connections, the omega network also supports broadcasting
Show Figure to explain the paths between source 2 and destinations 4,5,6 and 7

## Slide 7: Omega Network (Blocking)
Omega network is a blocking network
Because some permutations cannot be established by the network
For example, a permutation that requires
  source 3 to be connected to destination 1, and
  source 7 to be connected to destination 0
This cannot be established (Show figure)
However, such permutations can be established in several passes through the network
For example, when node 3 is connected to node 1, node 7 can be connected to node 0 through node 4
That is, node 7 sends its packet to node 4, and then node 4 sends the packet to node 0
Therefore, we can connect node 3 to node 1 in one pass and node 7 to node 0 in two passes

## Slide 8: Delta Network
Recapitulation of Floor Function and Ceiling Function
Floor(x) = Greatest integer ≤ x Floor(2.4) = 2
Ceil(x) = Least integer ≥ x Ceil(2.4) = 3
Mathematical definition of q-shuffle of qc objects (denoted by Sq*c):
Sq*c(i) = (qi + Floor(i/c)) mod qc for 0 ≤ i ≤ qc-1
Alternatively, Sq*c(i) = qi mod (qc-1) for 0 ≤ i < qc-1
= i for i = qc-1
Show diagram of a 4-shuffle of 12 indices viz. S4*3
2-shuffle is basically the well known perfect shuffle, discussed earlier

## Slide 9: Construction of an X bn Delta Network
An an X bn delta network has an sources and bn destinations
There are n stages consisting of a X b crossbar modules
a-shuffle is used as the link pattern between every two consecutive stages
Numbering of the stages is done as 1, 2, …., n starting at the source side
an-1 crossbar modules are required in the first stage
The first stage has an-1b output terminals and so the second stage must have an-1b input terminals
So stage 2 requires an-2b crossbar modules
The ith stage has an-ibi-1 crossbar modules of size a X b
Thus the total number of a X b crossbar modules required in an an X bn delta network can be found as:
(an - bn)/ (a – b) for a ≠ b
and, nbn-1 = nan-1 for a = b

## Slide 10: Construction of an X bn Delta Network
The stages are interconnected in such a fashion that there exists a unique path of constant length from any source to any destination
The path is digit controlled such that a crossbar module connects an input to one of its b outputs depending on a single base-b digit taken from the destination address
If the destination D is expressed in a base-b system as (dn-1dn-2 … d1d0)b, where D = d0b0 + d1b1 + …… + dn-1bn-1 and 0 ≤ di < b, then the base-b digit di controls the crossbar modules of stage (n-i)
No input or output terminal of any crossbar module is left unconnected
Show the diagram of 42 X 32, 23 X 23 and an X bn delta network

## Slide 11: Thank you