## Slide 1: Computer Architecture CSEN 3104 Lecture 2
Dr. Debranjan Sarkar

## Slide 2
Fetch next Instruction
Any Instruction to be executed?
Decode Instruction
Operand to be fetched?
Execute Instruction
Interrupt
to be processed?
More?
Start
Wait for next program
Transfer control to
Interrupt Service Routine (ISR)
Fetch operand
Yes
No
A Simple Instruction Cycle
Yes
Yes
No
Yes
No

## Slide 3: Instruction Execution Mechanism
A program is a set of instructions stored in memory
The program is executed in the computer by going through a cycle for each instruction
After the program is loaded onto the memory, the CPU fetches the first instruction
Then the instruction is decoded to understand what actions the instruction dictates
If required, it fetches the operand from the memory
Then the CPU carries out those actions i.e. executes the instruction
Contd….

## Slide 4: Instruction Execution Mechanism
If no interrupt is pending to be serviced, the control is transferred to the next instruction
In case some interrupt is pending to be serviced, the CPU transfers control to the Interrupt Service Routine (ISR)
After execution of the ISR, control is transferred to the next instruction (from where it came to ISR)
This cycle is repeated continuously by a computer's CPU, from boot up to shut down.
The fetch–decode–execute cycle (also known as instruction cycle) is the basic operational process of a computer

## Slide 5: Instruction Set Architecture
Instruction Format
Operation Code
  Example: Add, Sub, Complement etc.
Address field
  Memory location
  Processor Register
  Operand value
Mode
  Specifies the addressing mode to get the operand
  Effective address of the operand
  In some computer, no separate mode field and the addressing mode is specified in the instruction (opcode) itself
Example: ADD R1, R0
Operation Code
Mode
Address

## Slide 6: Instruction Set Architecture
In certain situations, special fields are used
  Number of shifts in a SHIFT type instruction
  Label field in a BRANCH type instruction
Memory or Registers store the operand values on which the instructions are executed
Memory addresses are used to specify operands stored in memory
A register address (k-bit) specifies one out of 2k registers in the CPU
A CPU with 32 registers has a register address field of 5 bits

## Slide 7: Thank you