## Slide 1: Computer Architecture CSEN 3104 Lecture 4
Dr. Debranjan Sarkar

## Slide 2: CISC vs. RISC Architecture
Complex Instruction Set Computer
(CISC)
More instructions for complex tasks
Complex instructions require relatively complex processing circuits, and too much expensive
More complex addressing modes (auto-increment, auto-decrement etc.)
Small number of General Purpose Registers (GPR)
Variable-length Instruction formats (spanning more than one word)
Less suitable for pipelining
Reduced Instruction Set Computer
(RISC)
Reduced number of instructions
This lowers processor cost, without much impact on performance.
Simple addressing modes (Register, Register indirect etc.)
Large register set
  uniform (no distinction between e.g. address and data registers)
All instructions have same length (one word)
More suitable for pipelining

## Slide 3: CISC vs. RISC Architecture
Complex Instruction Set Computer
(CISC)
Operands for the arithmetic / logic operations may be in the register or in memory
Memory-to-memory data transfer possible
Fewer instructions executed per program
Complex instructions reduce program size but does not necessarily translate into faster execution
Not constrained to load/store architecture. Typically use two-operand instruction format, with at least one operand in a register
Reduced Instruction Set Computer
(RISC)
Operands for the arithmetic / logic operations are always in the registers
Memory-to-memory data transfer not possible
More instructions executed per program
Though the program size is more, overall execution is faster
Instruction Set Architecture: Load/ store

## Slide 4: CISC vs. RISC Architecture
Complex Instruction Set Computer
(CISC)
As the number of memory access is more, the impact of von Neumann bottleneck is more
Mostly micro-programmed control units
Example of CISC (IBM 370/168, VAX 11/780, Intel x86, PDP-11, Motorola 68000 etc.)
Reduced Instruction Set Computer
(RISC)
Reduces the impact of von Neumann bottleneck by reducing the total number of the memory access made by the CPU
Mostly hardwired control unit
Example of RISC (MIPS, SUN Sparc, Intel i860, Motorola 88000, IBM RS6000, PowerPC, ARM etc.)

## Slide 5: MIPS ISA
Case Study

## Slide 6: MIPS (Microprocessor without Interlocked Pipelined Stages)
RISC Instruction Set Architecture
Developed by MIPS Computer Systems -> MIPS Technologies -> Wave Computing (since December 2018)
Multiple versions of MIPS
  MIPS I, II, III, IV and V (32 bit)
  MIPS32/64 (for 32- and 64-bit implementations, respectively) – six releases
MIPS is a modular architecture supporting up to four coprocessors (CP0/1/2/3)

## Slide 7: MIPS (Microprocessor without Interlocked Pipelined Stages)
CP0 is the System Control Coprocessor (an essential part of the processor)
CP1 is an optional floating point unit (FPU)
CP2/3 are optional implementation-defined coprocessors
For example, in the “PlayStation” video game console, CP2 is the Geometry Transformation Engine (GTE), which accelerates the processing of geometry in 3D computer graphics.
Originally, MIPS was designed for general-purpose computing.
During the 1980s and 1990s, MIPS processors were used for personal, workstation and server computers
MIPS processors are used in embedded systems such as residential gateways and routers

## Slide 8: Thank you