## Slide 1: Computer Architecture CSEN 3104 Lecture 5
Dr. Debranjan Sarkar

## Slide 2: MIPS Design Principles
Keep all instructions a single size
Always require three register operands in arithmetic instructions
Has only 32 registers
PC-relative addressing for conditional branches
Immediate addressing for constant operands

## Slide 3: MIPS: Registers and Memory
32 numbers of General Purpose Registers (32-bit each) (R0 to R31)
One 32-bit Program Counter (PC)
32 bit addressing capability for memory (capacity 4GB max)
Two views of memory:
  232 bytes with addresses 0, 1, 2, …, 232-1
  230 4-byte words with addresses 0, 4, 8, …, 232-4
Both views use byte addresses
Word address must be multiple of 4

## Slide 4: MIPS registers and usage
Each register may be referred to by number or name
Name | Register Number | Usage
$zero | 0 | The constant value 0
$at | 1 | Reserved for assembler
$v0 - $v1 | 2 – 3 | Values for results and expression evaluation
$a0 - $a3 | 4 – 7 | Arguments
$t0 - $t7 | 8 – 15 | Temporary registers
$s0 - $s7 | 16 – 23 | Saved registers
$t8 - $t9 | 24 – 25 | More temporary registers
$k0 - $k1 | 26 – 27 | Reserved for Operating System kernel
$gp | 28 | Global Pointer
$sp | 29 | Stack Pointer
$fp | 30 | Frame Pointer
$ra | 31 | Return Address

## Slide 5: MIPS Instructions
All instructions 1 word = 32 bits
3 different formats
Different formats for different purposes
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format

## Slide 6: MIPS Arithmetic & Logical Instructions
Manipulate data in registers
  Always 3 operands: destination + 2 sources
  Operand order is fixed
  Operands are always general purpose registers
  Instruction usage (assembly) add dest, src1, src2 dest=src1 + src2
  Example add $s1, $s2, $s3 $s1 = $s2 + $s3 or $s3, $s4, $s5 $s3 = $s4 OR $s5
  sub $s1, $s2, $s3 $s1 = $s2 - $s3 and $s3, $s4, $s5 $s3 = $s4 AND $s5

## Slide 7: Arithmetic & Logical Instructions (R-Format)
Used for arithmetic, logical, shift instructions
  op: Basic operation of the instruction (opcode) (Always 0 for R-Format)
  rs: first register source operand
  rt: second register source operand
  rd: register destination operand
  shamt: shift amount (0 when Not Applicable)
  funct: function code (identifies the specific R-format instruction)
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
0
31

## Slide 8: MIPS Data Transfer Instructions
Transfer data between registers and memory
Instruction format (assembly) lw $dest, offset($addr) load word sw $src, offset($addr) store word
Example
lw $s1, 100($s2) $s1 = Memory[$s2 + 100] sw $s1, 100($s2) Memory[$s2 + 100] = $s1
Uses:
  Accessing a variable in main memory
  Accessing an array element

## Slide 9: MIPS Data Transfer Instructions (I-Format)
Transfer data between registers and memory
Have a constant value immediately present in the instruction
Used for load, store instructions
  op: Basic operation of the instruction (opcode)
  rs: register containing base address
  rt: register destination/source
  offset: 16-bit signed address offset (-32,768 to +32,767)
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits

## Slide 10: MIPS Branch Instructions
Alter program flow beq $s1, $s2, 25 if ($s1==$s2) PC = PC + 4 + 4*25
Unconditional jump
j LABEL # goto Label
Conditional branches allow decision making
beq R1, R2, LABEL if R1==R2 goto LABEL bne R3, R4, LABEL if R3!=R4 goto LABEL
Example C Code if (i==j) goto L1; f = g + h; L1: f = f - i; Assembly beq $s3, $s4, L1 add $s0, $s1, $s2 L1: sub $s0, $s0, $s3

## Slide 11: MIPS Branch Instructions (I-Format)
Branch instructions use I-Format
Offset is added to PC when branch is effected beq r0, r1, offset has the effect: if (r0==r1) pc = pc + 4 + (offset << 2) else pc = pc + 4;
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Conversion to
word offset

## Slide 12: Comparisons - What about <, <=, >, >=?
bne, beq provide equality comparison
Slt dest, src1, src2 instruction sets dest if src1 < src2
slt $t0,$s3,$s4 # if $s3<$s4 $t0=1; here $t0 is the condition register # else $t0=0;
Combine Slt with bne or beq to branch if less than slt $t0,$s3,$s4 # if (a<b) bne $t0,$zero, Less # goto Less;
Why not include a blt instruction in hardware?
  Supporting in hardware would lower performance
  Assembler provides this function if desired (by generating the two instructions)

## Slide 13: Jump Instructions (J-Format)
Jump Instruction uses J-Format (op=2)
The 26 bits are achieved by dropping the high-order 4 bits of the address and the low-order 2 bits
The low order 2 bits are always 00, since addresses are always divisible by 4
What happens during execution?
PC = PC[31:28] : (IR[25:0] << 2)
jal (Jump and Link) Instruction has op=3
op
address
6 bits
26 bits
Conversion to
word offset
Concatenate upper 4 bits
of PC to form complete
32-bit address

## Slide 14: Constants / Immediate Instructions
Small constants are used quite frequently (50% of operands) e.g., A = A + 5; B = B + 1; C = C - 18;
MIPS Immediate Instructions (I-Format): addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4
Allows upto 16-bit constants, because
  16 bits fits neatly in a 32-bit instruction
  most constants are small (i.e. < 16 bits)
How do you load just a constant into a register?
    ori $5, $zero, 666
Arithmetic instructions sign-extend immediate data
Logical instructions don’t sign extend immediate data

## Slide 15: MIPS Logical Instructions
and, andi - bitwise AND
or, ori - bitwise OR
Example
and $s2,$s0,$s1 $s2 ← $s0 AND $s1
Bitwise AND the content of register $s0 with that of $s1 and put the result in register $s2
ori $s3,s2,252 $s3 ← $s2 OR 25210
Bitwise OR the content of register $s2 with 25210 and put the result in register $s3

## Slide 16: Loading 32-Bit Immediate data in a register
Normally, Immediate operations provide for 16-bit constants.
32-bit constant can be loaded in a register, using two instructions
Suppose we want to load in register $t0 the value 0A50FB2F016
load upper immediate - lui (I-Format) instruction is used to set the upper 16 bits of a constant in a register
After execution of the instruction
  lui $t0, 1010010100001111
The content of the register $t0 would be 0A50F000016 (lower 16 bits filled with 0)
Then ori instruction is used to fill in lower 16 bits
  ori $t0, $t0, 1011001011110000
After execution of this instruction
The content of the register $t0 would be 0A50FB2F016

## Slide 17: MIPS Shift Instructions
MIPS Logical Shift Instructions
  Shift left: sll (shift-left logical) instruction
  Right shift: srl (shift-right logical) instruction
Example
sll $s1,$s0,4 $s1 ← $s0 << 4 Shift left logical register $s0 by 4 bits and put the result in $s1
srl $s2,$s1,8 $s2 ← $s1 >> 8 Shift right logical register $s1 by 8 bits and put the result in $s2

## Slide 18: Thank You