## Slide 1: Computer Architecture CSEN 3104 Lecture 6
Dr. Debranjan Sarkar

## Slide 2: Basics of Pipelining

## Slide 3: Basics of pipelining
Modern CPUs employ a variety of speedup techniques viz.
  cache memory
  Pipelining etc..
Pipelining allows the processing of several instructions to be partially overlapped (parallelism)
Pipelining increases the overall instruction throughput.
All the common steps involved in instruction processing by the CPU can be pipelined:
  Instruction Fetching (IF)
  Instruction decoding (ID)
  Operand loading (OL)
  Execution (EX)
  Operand Storing (OS)

## Slide 4: Principles of Pipelining
Decomposes a sequential task into subtasks
Each subtask is executed in a special dedicated stage
These stages are connected with one another to form a pipe like structure.
Instructions enter from one end and exit from another end
Stages are pure combinational circuits for arithmetic or logic operations
Result obtained from a stage is transferred to the next stage
Final result is obtained after the instruction has passed through all the stages
Stages are separated by high speed latches (or registers)
All latches transfer data to the next stage simultaneously (on clock)
L
S3
L
S1
L
S2
Clock
Input
Output

## Slide 5: Instruction Processing : (a) Non-pipelined (b) Pipelined
Instruction Fetch (IF)
Instruction Decode (ID)
Operand Load (OL)
Execution (EX)
Operand Store (OS)
Time (clock cycles)
Instruction Fetch (IF)
Instruction Decode (ID)
Operand Load (OL)
Execution (EX)
Operand Store (OS)
Time (clock cycles)
IF1
IF2
IF3
IF4
IF5
IF6
IF7
IF8
IF9
IF10
IF11
ID1
ID2
ID3
ID4
ID5
ID6
ID7
ID8
ID9
ID10
OL1
OL2
OL3
OL4
OL5
OL6
OL7
OL8
OL9
EX1
EX2
EX3
EX4
EX4
EX5
EX6
EX7
EX8
OS1
OS2
OS3
OS4
OS5
OS6
1
2
3
4
5
6
7
8
9
10
12
11
13
14
15
IF1
IF2
IF3
ID1
ID2
ID3
OL3
OL2
OL1
EX1
EX2
EX3
OS1
OS2
OS3
1
3
4
5
6
7
8
9
10
11
12
13
14
15
2

## Slide 6: Pipelining
In the example, upto five instructions can be overlapped,
  provided, necessary pipeline stages are available
Example of performance reducing delays
  Instruction I4 (shaded) uses the EX stage for two consecutive cycles
  Instruction I7 (branch), where the outcome of the I7’s EX step must be known before the location of the next instruction (I8) to be processed can be identified.

## Slide 7: Performance measure of a pipeline
Speedup
Efficiency
Throughput

## Slide 8: Speedup of a pipeline
Let
  n be the number of input tasks,
  m the number of stages in the pipeline,
  P the clock period
The time required for the first input task to get through the pipeline = 1*m*P
The time required for the remaining tasks = (n-1)*1*P
Note that after the pipeline has been filled, it generates an output on each clock cycle.
Overall theoretical completion time (Tpipe) = m*P + (n-1)*P
The pipeline will greatly outperform nonpipelined techniques, which require each task to complete before another task’s execution sequence begins.

## Slide 9: Speedup of a pipeline
In a nonpipelined processor, the above sequential process requires a completion time of
Tseq = n * m * τ, where τ is the delay of each stage
If we ignore the small storing time tl that is required for latch storage (i.e., tl = 0), then
Tseq = n * m * P
Now, speedup (S) may be represented as:
S = Tseq / Tpipe = n*m / (m+n -1)
The value S approaches m when n→∞. That is, the maximum speedup, also called ideal speedup, of a pipeline processor with m stages over an equivalent nonpipelined processor is m
In other words, the ideal speedup is equal to the number of pipeline stages
That is, when n is very large, a pipelined processor can produce output approximately m times faster than a nonpipelined processor
When n is small, the speedup decreases. For n=1, the pipeline has the minimum speedup (= 1)

## Slide 10: Efficiency and Throughput of a pipeline
The efficiency E of a pipeline is defined as the speedup per stage
If m is the number of stages, then
E = S/m = [n*m / (m+n -1)] / m = n / (m+n -1)
The efficiency approaches its maximum value of 1 when n→∞
When n=1, E will have the value 1/m, which is the lowest obtainable value
The throughput H, also called bandwidth, of a pipeline is defined as the number of input tasks it can process per unit of time
When the pipeline has m stages, H is defined as
H = n / Tpipe = n / [m*P + (n-1)*P] = E / P = S / (mP)
When n→∞, the throughput H approaches the maximum value of one task per clock cycle

## Slide 11: Performance-cost-ratio of a pipeline
The number of stages in a pipeline often depends on the tradeoff between performance and cost
The optimal choice for such a number can be determined by obtaining the maximum value of a performance/cost ratio (PCR)
PCR is defined as the ratio of maximum throughput to pipeline cost
Throughput (H) =E /P
As the maximum value of efficiency (E) is 1, so maximum throughput is 1/P
Now P = (tseq/m) + tl
Thus the maximum throughput that can be obtained with such a pipeline is
1/P = 1/[(tseq/m) + tl]
The maximum throughput 1/P is also called the pipeline frequency
The actual throughput may be less than 1/P

## Slide 12: Performance-cost-ratio of a pipeline
The pipeline cost cp can be expressed as the total cost of logic gates (cg) and latches (m*cl) used in m number of stages.
cp = cg + m*cl
Note that the cost of gates and latches may be interpreted in different ways:
  Actual cost
  design complexity
  the area required on the chip or circuit board
PCR = 1/{[(tseq/m) + tl](cg + m*cl)}
This equation has a maximum value when m = sqrt {(tseq * cg) / (tl * cl)}
This value can be used as an optimal choice for the number of stages.

## Slide 13: Thank You