## Slide 1: Pipelined Architecture CSEN 3104 Lecture 7
Dr. Debranjan Sarkar

## Slide 2: Types of parallelism
Classification proposed by Wolfgang Handler (1977)
Parallelism and pipelining in 3 distinct levels
  Processor Control Unit (PCU) =>
    Processor or CPU
  Arithmetic Logic Unit (ALU) =>
    Functional Unit or a processing element (PE) in an array processor
    An element much smaller than a central processor and having much lower features than a processor
    working under the control of the processor
    there are many ALUs in a system, working in parallel to increase the speed of the system
  Bit Level Circuit (BLC) =>
    Combinational logic circuit needed to perform the bit operations in the ALU

## Slide 3: 3 Types of pipelining
Instruction pipelines
  Instruction Fetching (IF)
  Instruction decoding (ID)
  Operand loading (OL)
  Execution (EX)
  Operand Storing (OS)
Arithmetic pipelines
Processor pipelines
  a cascade of processors each executing a specific module in the application program

## Slide 4: Hazards of Instruction Pipeline
Situations preventing execution of the next instruction in the instruction stream during its designated clock cycle
The instruction is said to be stalled and a hazard is said to exist for that instruction
The instructions later in the pipeline are also stalled
Earlier instructions can continue
No new instructions are fetched during the stall
Pipeline cannot execute instructions at its peak rate
3 types of Hazards
  (1) Structural hazards
  (2) Data hazards
  (3) Control hazards

## Slide 5: Structural Hazards
A structural hazard refers to a situation in which a required resource is not available (or is busy) for executing an instruction.
Resource conflicts => Structural hazards
  use of same resource in different stages
Resource can be
  Memory (data and instruction)
  Functional Unit, which is not fully pipelined
Example: Let the ith instruction be ADD R4,X
Here Penalty = 1 cycle
Clock 1 2 3 4 5 6 7 8 9 10
ADD R4,X IF ID OF EX WB
(i+1)th instn IF ID OF EX WB
(i+2)th instn Stall IF ID OF EX WB
(i+3)th instn IF ID OF EX WB

## Slide 6: Structural Hazards
[1] If an execution unit that requires more than one clock cycle (such as multiply) is not fully pipelined or is not replicated, then a sequence of instructions that uses the unit cannot be subsequently (one per clock cycle) issued for execution.
Replicating and/or pipelining execution units increases the number of instructions that can be issued simultaneously.
[2] Another type of structural hazard that may occur is due to the design of register files.
If a register file does not have multiple write (read) ports, multiple writes (reads) to (from) registers cannot be performed simultaneously.
For example, under certain situations the instruction pipeline might want to perform two register writes in a clock cycle.
This may not be possible when the register file has only one write port.
The effect of a structural hazard can be reduced fairly simply by implementing multiple execution units and using register files with multiple input/output ports.

## Slide 7: Techniques to solve Structural Hazards
Certain resources are duplicated
Functional Units (ALU, FP unit) can be pipelined themselves in order to support several instructions at a time
Structural hazard due to memory conflict is avoided by providing separate data cache and instruction cache

## Slide 8: Data Hazards
A data hazard refers to a situation in which there exists a data dependency (operand conflict) with a previous instruction
Data dependencies => Data hazards
Example:
  Two instructions I1 and I2 are in pipeline
  The execution of I2 can start before I1 has terminated
  If I2 needs the result produced by I1, then there is a data hazard
Three classes of Data hazards
  RAW (read after write)
  WAR (write after read)
  WAW (write after write)
Read-after-Read (RAR) is not a hazard as no data is changed

## Slide 9: Data Hazards
delay = 3
previous
instr
current
instr
read/write
read/write

## Slide 10: Data Hazards: RAW (Read after Write)
Instruction (I): Write data object X
Instruction (J): Read data object X
J tries to read data before it is written by I
So, J gets old value of data which is incorrect
Program order must be preserved to ensure that J gets the correct data value

## Slide 11: Data Hazards: WAW (Write after Write)
Instruction (I): Write data object X
Instruction (J): Write (or modify) data object X
J tries to write (modify) data before it is written by I
So, finally the data object written by instruction I prevails which is not desirable
It was desired to have the final value of data object X written by instruction J and not by instruction I
Program order must be preserved to ensure that J gets the correct data value

## Slide 12: Data Hazards: WAR (Write after Read)
Instruction (I): Read data object X
Instruction (J): Write (or modify) data object X
J tries to write (modify) data object before it is read by I
So, the data object read by instruction I is incorrect
It was desired that instruction I would read the old value of X and then the data object would be modified by instruction J
Program order must be preserved to ensure that J gets the correct data value

## Slide 13: Thank you