## Slide 1: Pipelined Architecture CSEN 3104 Lecture 8
Dr. Debranjan Sarkar

## Slide 2: Data Hazards
A data hazard refers to a situation in which there exists a data dependency (operand conflict) with a previous instruction
Data dependencies => Data hazards
Example:
  Two instructions I1 and I2 are in pipeline
  The execution of I2 can start before I1 has terminated
  If I2 needs the result produced by I1, then there is a data hazard
Three classes of Data hazards
  RAW (read after write)
  WAR (write after read)
  WAW (write after write)
Read-after-Read (RAR) is not a hazard as no data is changed

## Slide 3: Data Hazards
delay = 3
previous
instr
current
instr
read/write
read/write

## Slide 4: Data Hazards: RAW (Read after Write)
Instruction (I): Write data object X
Instruction (J): Read data object X
J tries to read data before it is written by I
So, J gets old value of data which is incorrect
Program order must be preserved to ensure that J gets the correct data value

## Slide 5: Data Hazards: WAW (Write after Write)
Instruction (I): Write data object X
Instruction (J): Write (or modify) data object X
J tries to write (modify) data before it is written by I
So, finally the data object written by instruction I prevails which is not desirable
It was desired to have the final value of data object X written by instruction J and not by instruction I
Program order must be preserved to ensure that J gets the correct data value

## Slide 6: Data Hazards: WAR (Write after Read)
Instruction (I): Read data object X
Instruction (J): Write (or modify) data object X
J tries to write (modify) data object before it is read by I
So, the data object read by instruction I is incorrect
It was desired that instruction I would read the old value of X and then the data object would be modified by instruction J
Program order must be preserved to ensure that J gets the correct data value

## Slide 7: Detection of Data Hazards
Definitions:
  Resource Object: Working registers, memory locations, flags
  Data Object: Contents of the Resource Objects
  Domain of an Instruction D(I):
    Set of resource objects, whose data objects may affect the execution of the instruction I
    Holds the operands to be read for execution of the instruction
  Range of an Instruction R(I):
    Set of resource objects, whose data objects may be modified by the execution of the instruction I
    Holds the results produced after execution of the instruction

## Slide 8: Conditions for data hazards
I and J are two instructions in a program
I occurs before J
RAW Hazard: R(I) ∩ D(J) ≠ φ
WAW Hazard: R(I) ∩ R(J) ≠ φ
WAR Hazard: D(I) ∩ R(J) ≠ φ
These conditions are necessary (but not sufficient)
Hazard may not appear even if one or more of the above conditions are satisfied
If Hazard appears, then at least one of the above conditions must be satisfied
If the two instructions are executed in right order, hazard will not occur
D(J)
R(J)
D(I)
R(I)
D(J)
R(J)
R(I )
D(I)
D(I)
R(I)
D(J)
R(J)
Write (I)
Read (J)
Write (J)
Write (I)
Write (J)
Read (I)

## Slide 9: Detection of Data Hazard
Data hazard is detected in the Instruction Fetch (IF) stage of a pipeline
The domain and range of the fetched instruction is found out
The domain and range of other instructions, being processed in the pipeline, is found out
If any of the necessary conditions, stated earlier, is detected, a warning signal is issued to prevent the hazard from taking place

## Slide 10: Solution of Data Hazard: stall the pipeline
Let, a hazard has been detected between the current instruction (J) and a previous instruction (I)
Simple solution:
  Stall the pipeline and ignore the execution of the instructions J, J+1, J+2, …., until the instruction I has passed the point of resource conflict
Advanced solution:
  Ignore only instruction J and continue with the instructions J+1, J+2, ….
  The potential hazards due to the suspension of J must be continuously tested as the instructions J+1, J+2, … execute prior to J
  Multi-level hazard detection may be encountered, which requires very complex control policies

## Slide 11: Solution of Data Hazard: stall the pipeline
Example
Let, a hazard has been detected between the current instruction (J) and a previous instruction (I)
Instruction I: ADD R1, R2, R3
Instruction J: SUB R4, R1, R6
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
IF | I | J |  |  |  |  | 
ID |  | ADD | SUB |  |  |  | 
OF |  |  | R2, R3 | R1, R6 Delay | Delay | R1, R6 | 
EX |  |  |  | R2+R3 | R1-R6 |  | R1-R6
WB |  |  |  |  | Res to R1 |  | 
Delay 2 cycles

## Slide 12: Solution of Data Hazard: data forwarding
The data obtained at the Execution phase of the first instruction may be forwarded to the operand fetch unit of the 2nd instruction
Instruction I: ADD R1, R2, R3
Instruction J: SUB R4, R1, R6
After data forwarding, the delay is reduced to 1 cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
IF | I | J |  |  |  |  | 
ID |  | ADD | SUB |  |  |  | 
OF |  |  | R2, R3 | Delay | R2+R3 , R6 |  | 
EX |  |  |  | R2+R3 |  | R2+R3-R6 | 
WB |  |  |  |  | Res to R1 |  | 
Delay Reduced to 1 cycle
By Data Forwarding

## Slide 13: Control Hazards
A control hazard refers to a situation in which an instruction, such as branch, causes a change in the program flow
Procedural dependencies => Control hazards
  Instructions that change the content of program counter
  Example: unconditional and conditional branches, calls/returns
Processor cannot determine which instruction to fetch next until the branch instruction is executed completely
This causes delay in pipelined processors
Control hazards occur less frequently than data hazards

## Slide 14: Instruction Processing : (a) Non-pipelined (b) Pipelined with I7 as Jump instruction
Instruction Fetch (IF)
Instruction Decode (ID)
Operand Load (OL)
Execution (EX)
Operand Store (OS)
Time (clock cycles)
Instruction Fetch (IF)
Instruction Decode (ID)
Operand Load (OL)
Execution (EX)
Operand Store (OS)
Time (clock cycles)
IF1
IF2
IF3
IF4
IF5
IF6
IF7
IF8
IF9
IF10
IF11
ID1
ID2
ID3
ID4
ID5
ID6
ID7
ID8
ID9
ID10
OL1
OL2
OL3
OL4
OL5
OL6
OL7
OL8
OL9
EX1
EX2
EX3
EX4
EX4
EX5
EX6
EX7
EX8
OS1
OS2
OS3
OS4
OS5
OS6
1
2
3
4
5
6
7
8
9
10
12
11
13
14
15
IF1
IF2
IF3
ID1
ID2
ID3
OL3
OL2
OL1
EX1
EX2
EX3
OS1
OS2
OS3
1
3
4
5
6
7
8
9
10
11
12
13
14
15
2
Penalty : 3 cycles

## Slide 15: Techniques to mitigate Control Hazards: Freeze the pipeline
Freeze the pipeline
  until the branch outcome and target are known and then proceed with fetch
  incurs a penalty equal to the number of stall cycles
  unsatisfactory if
    the instruction mix contains many branch instructions
    the pipeline is very deep

## Slide 16: Techniques to mitigate Control Hazards: Pre-fetching
Pre-fetching
  Pre-fetch both the target instruction part and
  the instructions following the branch
  Multiport memory with concurrent access
  If a conditional branch is successful,
    Entire sequential prefetch buffer is invalidated
    Target prefetch buffer is validated
  And vice versa
  When instruction is requested by the decoder,
    It enters the decoder from one of the Prefetch Buffers
    depending on the situation
    No delay is incurred
  Otherwise, the decoder is idle until the instruction comes from memory
Sequential Prefetch Buffer
Target Prefetch Buffer
Decoder
1
Memory System
2
3
4

## Slide 17: Techniques to mitigate Control Hazards: Branch Prediction
Uses some additional logic (heuristic) to predict the outcome of a conditional branch instruction before it is executed
Normally two strategies are followed
  Static Branch Strategy: Probability of branch
  Dynamic Branch Strategy: Branch history is taken into consideration
Instructions are speculatively fetched and executed down the predicted path
But results are not written back to the register file until the branch is executed and the prediction is verified
When a branch is predicted, the processor enters a speculative mode in which results are written to another register file that mirrors the architected register file
Another pipeline stage called the commit stage is introduced to handle writing verified speculatively obtained results back into the "real" register file
Branch predictors cannot be 100% accurate
So there is still a penalty for branches if the prediction is found to be incorrect

## Slide 18: Techniques to mitigate Control Hazards: Delayed Branch
The compiler detects the branch instruction and rearranges the machine language code sequence by inserting useful instructions or NOPs (No operations) that keep the pipeline operating without interruptions
The Assembly Language Program developer must fill these branch delay slots
This causes the computer to fetch the target instruction during the execution of the other useful instructions (or NOPs), allowing a continuous flow of the pipeline
This solution does not extend well to deeper pipelines

## Slide 19: Example of Delayed Branch
I1: Load R1, A
I2: Decrement R3, 1
I3: Branch zero R3, I5
I4: Add R2, R4
I5: Subtract R5, R6
I6: Store R5, B
  Original Program
I2: Decrement R3, 1
I3: Branch zero R3, I5
I1: Load R1, A
I4: Add R2, R4
I5: Subtract R5, R6
I6: Store R5, B
  Reordered Instructions

## Slide 20: Example of Delayed Branch
By reordering, I1, I4, and I5 are executed regardless of the branch outcome
If the branch is unsuccessful,
  Produces the same results as the original program
If the branch is successful,
  Execution of delayed instructions I1 and I5 needed anyway
  Only one cycle is wasted in executing instruction I4, which is not needed
In case of 5-stage instruction pipeline:
  The delay slot is reduced to 1 for an unsuccessful branch
  The delay slot is reduced to 2 for a successful branch

## Slide 21: More about Delayed Branch
Data dependencies between instructions moving across the branch and the remaining instructions being scheduled must be analyzed
Instructions I1 and I4 are independent of the remaining instructions (I2, I3, I5 and I6), leaving them in the delay slot will not create data hazards
Inserting NOP fillers does not save any cycles in the delayed branch operation
Delayed branching is more effective in short instruction pipelines with about four stages
Delayed branching is implemented in most RISC processors, including MIPS R4000

## Slide 22: Classification of pipelines
As per Configuration, pipelines are of two types:
Static Pipeline:
  A static pipeline can perform only one function (or operation such as addition or multiplication) at a time
  The operation of a static pipeline can only be changed after the pipeline has been drained
  A pipeline is said to be drained when the last input data leave the pipeline
  Thus, the performance of static pipelines is severely degraded when the operations change often
Dynamic Pipeline:
    a dynamic pipeline can perform more than one function at a time

## Slide 23: Reservation Table
A pipeline reservation table shows when stages of a pipeline are in use for a particular function
Each stage of the pipeline is represented by a row in the reservation table
Each column of the reservation table represents one clock cycle
The number of columns indicates the total number of time units required for the pipeline to perform a particular function.
To indicate that some stage S is in use at some time ty, an X is placed at the intersection of the row and column in the table corresponding to that stage and time
Multiple checkmarks in a row, means repeated usage of the same stage in different cycles

## Slide 24: Reservation Table
3 stages, 5 clock cycles
The input data goes through the stages 1, 2, 2, 3 and 1 progressively
A static pipeline and its corresponding reservation table.

## Slide 25: Thank you