## Slide 1: Pipelined Architecture CSEN 3104 Lecture 9
Dr. Debranjan Sarkar

## Slide 2: Reservation Table
3 stages, 5 clock cycles
The input data goes through the stages 1, 2, 2, 3 and 1 progressively
A static pipeline and its corresponding reservation table.

## Slide 3: Scheduling of Static Pipelines

## Slide 4: Pipeline Control: Scheduling
Controlling the sequence of tasks presented to a pipeline for execution is extremely important for maximizing its utilization.
If two tasks are initiated requiring the same stage of the pipeline at the same time, a collision occurs, which temporarily disrupts execution.
The reservation table can be used for determining the time difference between input data initiations so that collisions won't occur.
Initiation of an input data refers to the time that the data enter the first stage of the pipeline.

## Slide 5: Some Definitions
Initiation: Launching of an operation into the pipeline. i.e. the time that the data enter the first stage of the pipeline
Latency: the delay (or, the number of cycles) that elapse between two initiations of a pipeline
Latency values must be non-negative integers
A collision will occur if two pieces of input data are initiated with a latency equal to the distance between two X's in a reservation table
For example, the reservation table, shown earlier, has two X's with a distance of 1 in the second row
So, if a second piece of data is passed to the pipeline one time unit after the first, a collision will occur in stage 2
A latency value k means that two initiations are separated by k clock cycles

## Slide 6: Some definitions
Collision
  Collision occurs if a stage in the pipeline is required to perform more than one task at any time
  Any attempt by two or more initiations to use the same pipeline stage at the same time will cause a collision.
  A collision will occur if two pieces of input data are initiated with a latency equal to the distance between two X's in a reservation table
  For example, the reservation table, shown earlier, has two X's with a distance of 1 in the second row
  Therefore, if a second piece of data is passed to the pipeline one time unit after the first, a collision will occur in stage 2
  A collision implies resource conflicts between two initiations in the pipeline, so it should be avoided

## Slide 7: Forbidden Latency
Latencies that cause collision are called forbidden latencies
Forbidden latencies should be prohibited
Otherwise, the two data would arrive at the same stage of the pipeline at the same time and lead to collision
Forbidden latencies for the previous RT are 1 and 4
Let the Maximum forbidden latency be m (here 4)
n = no. of columns (m ≤ n-1)
With static pipelines, zero is always considered a forbidden latency, since it is impossible to initiate two jobs to the same pipeline at the same time.
However, such initiations are possible with dynamic pipelines

## Slide 8: Permissible Latency
Latencies that do not cause any collision are called permissible latencies
Permissible latencies for the previous RT are 2 and 3, as they do not cause collision
Let the Maximum forbidden latency be m
All the latencies greater than m do not cause collisions
Permissible Latency p, lies in the range 1 ≤ p ≤ m-1
Value of p should be as small as possible
Permissible latency p=1 corresponds to an ideal case, can be achieved by a static pipeline

## Slide 9: Forbidden Latency set or Forbidden List
Reservation table, having more than one X's in any given row, has one or more forbidden latencies, which, if not prohibited, would allow two data to collide or arrive at the same stage of the pipeline at the same time
Forbidden Latency set: the set of all possible column distances between two entries in a particular row of Reservation Table
The forbidden list F is simply a list of integers corresponding to these prohibited Latencies
As 0 is always considered a forbidden latency for static pipelines, 0 may be included in the Forbidden List

## Slide 10: Collision Vectors
A collision vector is a combined set of permissible and forbidden latencies.
Let the Maximum forbidden latency be m (here 4) and n = no. of columns (m ≤ n-1)
Then the collision vector is an m-bit binary number C = (Cm Cm-1….C2 C1 )
The initial collision vector, C, is created from the forbidden list in the following way:
  each component Ci of C, for i=1 to m, is 1 if i is an element of the forbidden list.
  Otherwise, Ci is zero

## Slide 11: Example 1
Forbidden Latency Set, F = {5} U {2} U {2} = { 2,5}
Permissible Latency List = { 1,3,4}
Initial Collision Vector = 10010

## Slide 12: State Diagram
State Diagram is a graph of all the possible operation sequences through the pipeline
State diagrams can be constructed to specify the permissible transitions among successive initiations
State diagrams can be used to show the different states of a pipeline for a given time slice
Once a state diagram is created, it is easier to derive schedules of input data for the pipeline that have no collisions

## Slide 13: Procedure for construction of State Diagram
Start with the ICV
For each unprocessed state,
For each bit i in the CVi which is 0, do the following:
Shift CVi right by i bits
Drop i rightmost bits
Append zeros to left
Logically OR with ICV
If step(d) results in a new state then form a new node for this state and join it with node of CVi by an arc with a marking i.
This shifting process needs to continue until no more new states can be generated.

## Slide 14: Example 1: State Diagram
1 0 0 1 0

## Slide 15: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
ICV – 10010 OR
CVi – 01001
CV* 11011
i = 1
1

## Slide 16: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
ICV – 10010 OR
CVi – 00010
CV* 10010
i = 3
3

## Slide 17: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
1 0 0 1 1
4
3
ICV – 10010 OR
CVi – 00001
CV* 10011
i = 4

## Slide 18: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
1 0 0 1 1
4
3
ICV – 10010 OR
CVi – 00000
CV* 10010
i = 5
6+

## Slide 19: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
1 0 0 1 1
4
3
ICV – 10010 OR
CVi – 00010
CV* 10010
i =3
6+
3

## Slide 20: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
1 0 0 1 1
4
3
ICV – 10010 OR
CVi – 00001
CV* 10011
i =4
6+
3
4

## Slide 21: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
1 0 0 1 1
4
3
ICV – 10010 OR
CVi – 00011
CV* 10011
i =3
6+
3
4
3

## Slide 22: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
1 0 0 1 1
4
3
ICV – 10010 OR
CVi – 00000
CV* 10010
i = 5
6+
3
4
3
6+

## Slide 23: Example 1: State Diagram
1 0 0 1 0
1 1 0 1 1
1
1 0 0 1 1
4
3
ICV – 10010 OR
CVi – 00000
CV* 10010
i = 5
6+
3
4
3
6+
6+

## Slide 24: Cycle, Average Latency and MAL
A cycle in a state diagram is an alternating sequence of collision vectors and arcs: C0, a1, C1, ..., an, Cn
Each arc ai connects collision vector Ci-1 to Ci
All the collision vectors are distinct except the first and last
A cycle is simply represented by a sequence of latencies of its arcs
A Constant Cycle is a latency cycle which contains only one latency value
The average latency for a cycle is determined by adding the latencies of the arcs of the cycle and then dividing it by the total number of arcs in the cycle
Minimum Average Latency (MAL) is the minimum of all the average latencies of a state diagram

## Slide 25: Example 1: Average Latency
Let C0 is 10010, C1 is 11011 and C2 is 10011
The cycle C0, a1, C1, a2, C2, a3, C0
a1 is an arc (latency = 1) from C0 to C1
a2 is an arc (latency = 3) from C1 to C2
a3 is an arc (latency = 6) from C2 to C0
The cycle is represented as C=(1, 3, 6)
The average latency for a cycle is determined by adding the latencies of the arcs of the cycle and then dividing it by the total number of arcs in the cycle
The cycle C=(1, 3, 6) has the average latency:
(1 + 3 + 6)/3 = 3.33

## Slide 26: Example 1: Minimum Average Latency (MAL)
The following are the average latencies of the different cycles in example 1
3/1= 3
6/1= 6
(1 + 6)/2 =3.5
(1 + 3 + 3)/3 =2.33
(1 + 3 + 6)/3 = 3.33
(4 + 3)/2 = 3.5
(4 + 6) /2 = 5
4/1 = 4
The minimum average latency is simply the minimum of these values
So the MAL is 2.33

## Slide 27: Thank you